## Slide 1: Scientific Machine Learning and Tensorflow tutorial
Operator Learning
SAND2024-00936O
Ravi G Patel
Scientific Machine Learning Department
February 1 – 2, 2024
Numerical PDEs: Analysis, Algorithms, and Data Challenges
ICERM
Brown University

## Slide 2: Physical systems are described by PDE’s
We describe many physical systems with fields, i.e., functions over a spatio-temporal domain
When we model field data, we’re trying to find a unknown PDE
  An equation with field valued solutions that match our data
  Historical examples,
Physics | Incompressible fluid | Electromagnetism | Elasticity
Fields | Fluid velocity | Fluid velocity | Stress/strain
PDE | Navier-Stokes | Electric/magnetic | Hook’s Law
Forced isotropic turbulence JHTDB, turbulence.pha.jhu.edu
Cantilever bean under gravity FENICS, fenicsproject.org
Magnetic field from oscillating current Elmer FEM, elmerfem.org

## Slide 3: PDE modeling is hard
Multiphase, multiphysics problems
  Can’t easily model with intuition
  Data driven methods provide an alternative
Reynolds stress modeling for single phase turbulence
Forced isotropic turbulence JHTDB, turbulence.pha.jhu.edu

## Slide 4: PDE modeling is hard
Multiphase, multiphysics problems
  Can’t easily model with intuition
  Data driven methods provide an alternative
Reynolds averaged transport equations1 for particle-laden turbulent flow
1Capecelatro et al., J. Fluid Mech. (2015)
Granular temperature field in cluster-induced turbulence1

## Slide 5: PDE modeling is hard
Multiphase, multiphysics problems
  Can’t easily model with intuition
  Data driven methods provide an alternative
Reynolds averaged transport equations1 for particle-laden turbulent flow
1Capecelatro et al., J. Fluid Mech. (2015)
Granular temperature field in cluster-induced turbulence1
Adding a single extra phase greatly complicates the model
Need a scalable approach to PDE modeling

## Slide 6: Operator learning enables PDE discovery
PDE’s are composed of operators, i.e., mappings between functions,
E.g., the viscous Burger’s equation has three operators,
If we’re given the field data, we can find a PDE by finding it’s component operators

## Slide 7: Operator learning is a generalization of regression
Fitting operators
Fitting functions
Given pairs of functions, , we can use regression to find the operator maps between the two,

## Slide 8: Three Components of an operator learning method
A discretization for functional data
  To run on computers, we need to work with some discretization
  Usually implicit in the dataset we receive
  Often taken to be point evaluations of the functions
An interpolation scheme
  Even though we only work with discretizations, we should be able to evaluate the functions anywhere they’re defined
  Can be learned or fixed
A parameterized mapping between discretizations
  We’ll use gradient based methods to optimize these parameters against the error norm

## Slide 9: Operator learning parameterizations
Modal operator regression for physics (MOR-Physics1,2)
Given pairs of functions, , let’s find a Poisson-like PDE,
  Let’s assume they’re given as point-wise evaluations on a regular, periodic grid
We parameterize the unknown operator as,
Where and are neural networks. is the Fourier transform
Optimization problem becomes,
    1R.G. Patel and Desjardins, arxiv: 1810.08552 (2018)
    2R.G. Patel et al., CMAME (2021)

## Slide 10: MOR-Physics: motivation
For smooth functions in a periodic domain,
Parameterization contains,
Laplacian
Physical space
Fourier space
Burgers operator

## Slide 11: MOR-Physics: Example
MOR-Physics parameterization1
MOR-physics learns dynamics of colloidal system from molecular dynamics simulations. Generalizes to unseen concentration and colloid diameter2
    1R.G. Patel and Desjardins, arxiv: 1810.08552 (2018)
    2R.G. Patel et al., CMAME (2021)

## Slide 12: Operator learning parameterizations
Deep Operator Network (DeepONet)1
Given pairs of functions, , let’s find a Poisson-like PDE,
  Let’s assume they’re given as point-wise evaluations on two (possibly different) sets of collocation points
We parameterize the unknown operator as,
Where and are neural networks
Optimization problem becomes,
1Lu, Jin and Karniadakis, Nature, 2021

## Slide 13: DeepOnet example
Variational DeepONet learns crack path under shear loading. Generalizes to unseen crack tip locations.2
Unstacked DeepONet parameterization
1Lu, Jin and Karniadakis, Nature, 2021 2Goswami et al., CMAME, 2022

## Slide 14: Including a priori knowledge
Operator learning is flexible
  Can learn several operators simultaneously
  Can combine a partially known PDE with unknown operators
Often, we’ll know more about a system than just that the data
  Theoretical results
  Symmetries
  Conservation principles

## Slide 15: Time evolving systems
Assume system is described by 1st order in time, autonomous PDE,
Discretize in time,
Given observations, , find,
More generally,

## Slide 16: Time evolving systems
Alternatively, parameterize your operator with time
Lu, Jin and Karniadakis, Nature, 2021
Li et al., ICLR (2021)

## Slide 17: Other operator learning frameworks and Related methods
Fourier Neural Operator
  Li et al., ICLR (2021)
Nonlocal operator regression
  H. You et al., CMAME (2020)
Operator Inference
  B. Peherstorfer and K. Willcox, CMAME (2016)
Function-to-function regression
  J.S. Morris, Annu. Rev. Stat. Appl. (2015)